## Slide 1: Ali Abd El-Fattah
Smart Home Project

## Slide 2: Contents:
Project Purpose.
Project Description.
Project Tools.
Hardware Connections.
Software Explanation.
Project Configuration.
Summary.

## Slide 3: Project Purpose
The main purpose of the project is to control your home using only your cell phone

## Slide 4: Project Description
The project consists of two microcontrollers (Master and Slave) connected together through SPI.
The Master microcontroller is connected to the cell phone through UART using Bluetooth module.
The data sent from the cell phone perform changes to your home.
The home is represented as 1 room.
The room consists of (Light , Television and Air conditioner).
Light and Television is represented by a led.
Air conditioner is represented by a led and external (AC) Lamp.

## Slide 5: Project Tools
2 Microcontrollers (AT mega 32).
Bluetooth Module (HC-06).
6 LEDs.
Relay (5 VDC).
Buzzer.
2 LCDs (16x2).
Lamp (220 VAC).
5 Connectors (Female – Female).
Smart Phone.

## Slide 6: Hardware Connections
Master (CLK) connected to Slave (CLK).
Master (MOSI) connected to Slave (MOSI).
Master (MISO) connected to Slave (MISO).
Slave (SS) connected to Slave (Gnd).
Master (Gnd) connected to Slave (Gnd).
Bluetooth Module connected to (UART) PORT in Master:
Bluetooth (VCC) Connected to UART (VCC) Pin.
Bluetooth (Gnd) Connected to UART (Gnd) Pin.
Bluetooth (TX) Connected to UART (RX) Pin.
Bluetooth (RX) Connected to UART (TX) Pin.

## Slide 7: Software Explanation
Use Bluetooth module to transmit data to the Master microcontroller
with communication protocol ( UART ).
Then send data from Master microcontroller to Slave microcontroller
with communication protocol ( SPI ).
Perform the written code in Master microcontroller.
Perform the written code in Slave microcontroller.

## Slide 8: Project Configuration
Light ON Send ‘1’ From your Cell Phone.
Light OFF Send ‘2’ From your Cell Phone.
TV ON Send ‘3’ From your Cell Phone.
TV OFF Send ‘4’ From your Cell Phone.
AC ON Send ‘5’ From your Cell Phone.
AC OFF Send ‘6’ From your Cell Phone.
All OFF Send ‘7’ From your Cell Phone.

## Slide 9: Summary
The project is divided into 2 Folders:
Master
Slave
Each Folder Contains 4 Folders:
LIB (STD_TYPES , BIT_MATH)
MCAL (DIO , SPI , UART)
HAL (LCD)
APP (main)